## Slide 1
Jason Stewart (AMD) | Rolando Caloca O. (Epic Games) | 21 March 2018
Taking the Red Pill – Using Radeon GPU Profiler to look inside your game
(With Bonus UE4 Vulkan Update from Epic)

## Slide 2
Jason Stewart (AMD) | Rolando Caloca O. (Epic Games) | 21 March 2018
Taking the Red Pill – Using Radeon GPU Profiler to look inside your game
(With Bonus UE4 Vulkan Update from Epic)

## Slide 3
agenda
Radeon GPU Profiler walkthrough with examples from UE4 Vulkan | Jason Stewart (AMD)
UE4 Vulkan update | Rolando Caloca O. (Epic Games)

## Slide 4
Radeon GPU Profiler walkthrough
With examples from UE4 Vulkan
Jason Stewart (AMD)

## Slide 5
What is Radeon GPU Profiler?
Quick Start Guide
GPU Profiler
Analyze. Adjust. Accelerate.
Notes: <number>

## Slide 6
Detailed workload information
DX12 and Vulkan support
Hardware level profiling features
What is Radeon GPU Profiler?
Quick Start Guide

## Slide 7
RGP support is built directly into the production driver
Quick Start Guide

## Slide 8
RGP is available for free on GitHub as part of gpuopen
Quick Start Guide

## Slide 9
More information on gpuopen.com
Quick Start Guide
https://gpuopen.com/tag/rgp/
https://gpuopen.com/gaming-product/radeon-gpu-profiler-rgp/
Or just Google on Radeon GPU Profiler

## Slide 10
How to capture a profile
Quick Start Guide
Connect
Notes: Connect Radeon Developer Panel to Radeon Developer Service
Set up the target application

## Slide 11
How to capture a profile
Quick Start Guide
Capture
Notes: Launch the target application
RGP support is built directly into the production driver
Capture a trace
Double click to open in RGP

## Slide 12
Refer to the built-in help for more information
Quick Start Guide
Help

## Slide 13
Refer to the built-in help for more information
Quick Start Guide

## Slide 14
One slide to talk about RGP/RenderDoc Interop
Only one slide, because there will have been a full talk on this on the same day just a few hours earlier
Mention the UE4 works out of the box with RGP and RenderDoc
  e.g. frame markers get enabled automatically
Needs 18.10 or newer driver
RGP/RenderDoc Interop
Notes: VK_EXT_debug_marker, vkCmdDebugMarkerBeginEXT, vkCmdDebugMarkerEndEXT
EnableIdealGPUCaptureOptions
<number>

## Slide 15
Where to start
Viewing a capture in RGP
Notes: SunTemple at 1080p with vsync enabled, present bound
18.10 driver includes present packets in the system activity display
This slide is to point out the new present packet display and to emphasize that you want to get out of this situation (vsync bound) when profiling
For profiling, prefer VK_PRESENT_MODE_IMMEDIATE_KHR (i.e. disable vsync)?
If so, can we do this automatically in UE4 code, like we enable frame markers?
<number>

## Slide 16
Where to start
Viewing a capture in RGP
Placeholder
Notes: Show no vsync, but still not right
Broken query system, for example
<number>

## Slide 17
Where to start
Viewing a capture in RGP
Notes: You want to see something more like this
Vsync disabled, no CPU-GPU sync points, no GPU idle time, GPU bound
You want to make sure you have this part right, the CPU-side feeding of the GPU, before continuing
<number>

## Slide 18
Where to start
Viewing a capture in RGP
Notes: Barrier reason codes
Also mention that fast clear eliminate and init mask RAM are to be expected
But you want to try to avoid the other cases
Depth/stencil decompress, DCC decompress, etc.
<number>

## Slide 19
Talk about the other things available in the overview tab
  Most expensive events
  Context rolls
  Device configuration
This part might be brief, depending on if we have any particularly interesting UE4 Vulkan examples to talk about
Where to start
Viewing a capture in RGP

## Slide 20
Event Timing
Notes: Do before and after depth bounds test
Frame it in the context of making sure any DX-only optimizations are brought over to your Vulkan path
<number>

## Slide 21
Wavefront Occupancy
Occupancy
Graph
GPU
Events

## Slide 22
What’s a wavefront?
Wavefront Occupancy
?

## Slide 23
X Shader Engines per Chip with Y Compute Units per Shader Engine
GCN Architecture
Notes: This particular diagram is for Polaris, specifically Polaris10 "Ellesmere“, i.e. RX 480/580
<number>

## Slide 24
X Shader Engines per Chip with Y Compute Units per Shader Engine
GCN Architecture
Notes: This particular diagram is for Polaris, specifically Polaris10 "Ellesmere“, i.e. RX 480/580
<number>

## Slide 25
X Shader Engines per Chip
GCN Architecture
Notes: RX 580 has this configuration
Compute Units: 36
ROPs: 32
Stream Processors: 2304
Texture Units: 144
Once pixels have been shaded, they are typically sent to the render back-ends (RBs) for depth and stencil tests and any blending before the final output to the display
36 CUs with 4 SIMDs per CU and a 16x VALU per SIMD that can do 2 floating point ops per clock equals …
36×4×16=2304 Stream Processors
2304×2=4608 FLOPs per clock
4608 FLOPs per clock at 1340 MHz boost clock equals …
4608×1340000000=6174720000000
6.2 TFLOPs
<number>

## Slide 26
X Shader Engines per Chip with Y Compute Units per Shader Engine
GCN Architecture
Notes: RX 580 has this configuration
Compute Units: 36
Stream Processors: 2304
Texture Units: 144
36 CUs with 4 SIMDs per CU and a 16x VALU per SIMD that can do 2 floating point ops per clock equals …
36×4×16=2304 Stream Processors
2304×2=4608 FLOPs per clock
4608 FLOPs per clock at 1340 MHz boost clock equals …
4608×1340000000=6174720000000
6.2 TFLOPs
<number>

## Slide 27
Y Compute Units per Shader Engine
GCN Architecture
Notes: RX 580 has this configuration
Compute Units: 36
Stream Processors: 2304
Texture Units: 144
<number>

## Slide 28
4 SIMD Units per CU
GCN Compute Unit
Scheduler
Tex
Tex
Tex
Tex
L1
SALU
SGPR
VALU
VGPR
LDS
Branch & Message Unit
VALU
VGPR
VALU
VGPR
VALU
VGPR
Notes: <number>

## Slide 29
4 SIMD Units per CU
GCN Compute Unit
Scheduler
Tex
Tex
Tex
Tex
L1
SALU
SGPR
VALU
VGPR
LDS
Branch & Message Unit
VALU
VGPR
VALU
VGPR
VALU
VGPR
Notes: <number>

## Slide 30
4 SIMD Units per CU
GCN Compute Unit
VALU
VGPR
VALU
VGPR
VALU
VGPR
VALU
VGPR
Notes: <number>

## Slide 31
4 SIMD Units per CU
GCN Compute Unit
VALU
VALU
VGPR
VGPR
VALU
VALU
VGPR
VGPR
SIMD
SIMD
SIMD
SIMD
Notes: <number>

## Slide 32
What’s a wavefront?
GCN Compute Unit
SIMD
SIMD
SIMD
SIMD
Notes: <number>

## Slide 33
SIMD = Single instruction, multiple data
What’s the multiple?
  The GPU works on 64-thread groups called wavefronts (or waves)
  Smallest unit of GPU work
  Each wavefront shares a single program counter
Each SIMD is executing an independent wavefront
16-lane vector ALU per SIMD
  Each SIMD cycles through the 64 work items in a wavefront
What’s a wavefront?
GCN Compute Unit
SIMD
SIMD
16-lane vector ALU
64KB VGPR Memory
Notes: A wavefront or wave is a collection of 64 work items grouped for efficient processing on the compute unit
Each wavefront shares a single program counter
Each SIMD is executing an independent wavefront
Each SIMD includes a 16-lane vector pipeline
Each SIMD simultaneously executes a single operation across 16 work items (threads)
A wavefront is issued to a SIMD in a single cycle, but takes 4 cycles to execute operations for all 64 work items
That is, each SIMD operates on wavefronts of 64 work-items over four clock cycles
Many wavefronts can be processed in parallel
<number>

## Slide 34
A GCN Compute Unit supports having up to 8 or 10 wavefronts in flight per SIMD “at once”
Helps hide memory latency
Compute Unit scheduler can switch to another wavefront on a SIMD when a memory fetch stalls a shader program
Multiple Waves in flight per SIMD
GCN Compute Unit
SIMD
16-lane vector ALU
64KB VGPR Memory
Wave 0
Wave 1
Wave 2
Wave 3
Wave 4
Wave 5
Wave 6
Wave 7
Notes: A wavefront or wave is a collection of 64 work items grouped for efficient processing on the compute unit
Each wavefront shares a single program counter
Each SIMD is executing an independent wavefront
Each SIMD includes a 16-lane vector pipeline
Each SIMD simultaneously executes a single operation across 16 work items (threads)
A wavefront is issued to a SIMD in a single cycle, but takes 4 cycles to execute operations for all 64 work items
That is, each SIMD operates on wavefronts of 64 work-items over four clock cycles
Many wavefronts can be processed in parallel
<number>

## Slide 35
A GCN Compute Unit supports having up to 8 or 10 wavefronts in flight per SIMD “at once”
Helps hide memory latency
Compute Unit scheduler can switch to another wavefront on a SIMD when a memory fetch stalls a shader program
Multiple Waves in flight per SIMD
GCN Compute Unit
16-lane vector ALU
Wave 0
Wave 1
Wave 2
Wave 3
Wave 4
Wave 5
Wave 6
Wave 7
Wave 0
Wave 1
Notes: A wavefront or wave is a collection of 64 work items grouped for efficient processing on the compute unit
Each wavefront shares a single program counter
Each SIMD is executing an independent wavefront
Each SIMD includes a 16-lane vector pipeline
Each SIMD simultaneously executes a single operation across 16 work items (threads)
A wavefront is issued to a SIMD in a single cycle, but takes 4 cycles to execute operations for all 64 work items
That is, each SIMD operates on wavefronts of 64 work-items over four clock cycles
Many wavefronts can be processed in parallel
<number>

## Slide 36
Several traces from UE4 will be shown
Live Demo
Wavefront Occupancy

## Slide 37
One slide on why, if lower VGPR usage is desirable, why doesn’t the AMD driver shader compiler just force lower VGPR usage
WavefronT Occupancy

## Slide 38
Refer to the built-in help for more information
Radeon GPU Profiler
Help

## Slide 39
Refer to the built-in help for more information
Radeon GPU Profiler

## Slide 42
Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2018 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names are for informational purposes only and may be trademarks of their respective owners.

## Slide 43
UE4 Vulkan update
Rolando Caloca O. (Epic Games)

## Slide 44
Backup slides

## Slide 45
Compute Units: 36
Base Frequency: Up to 1257 MHz
Boost Frequency: Up to 1340 MHz
Peak Pixel Fill-Rate: Up to 42.88 GP/s
Peak Texture Fill-Rate: Up to 192.96 GT/s
Max Performance: Up to 6.2 TFLOPs
ROPs: 32
Stream Processors: 2304
Texture Units: 144
Transistor Count: 5.7 B
Specs
Radeon RX 580